## Slide 1: The iLoc Location Algorithm
István Bondár
Research Centre for Astronomy and Earth Sciences, Hungarian Academy of Sciences
Training in Network Management Systems and Analytical Tools for Seismology
Baku, Azerbaijan, 23-27 October 2017

## Slide 2: iLoc
Based on the ISC location algorithm (Bondár and Storchak, 2011)
While retaining the main features of the ISC locator, iLoc focuses on the needs of
  local and regional network operators
  NDCs
  global location studies
iLoc is open source
Available for download from the ORFEUS seismological software library
  http://www.orfeus-eu.org/website_until_17aug2016/software.html
  http://www.seismology.hu/data/iLoc/
  Current version is 1.60

## Slide 3: Motivation
Error ellipses are often unreliable due to the violation of assumptions of independent, Gaussian errors.
  Similar ray paths introduce correlated systematic travel time prediction errors!
Ignoring correlated errors results in
  Underestimated error ellipses
  Increasing location bias with increasing number of stations
Lop Nor nuclear explosion, 10/7/1994: mislocation, error ellipse and GT coverage with increasing number of stations
Coverage is less than 1 if GT location falls inside the error ellipse
90% error ellipse area
GT coverage
network
mislocation
GT1

## Slide 4: The locator in a nutshell (ISC algorithm)
Uses most ak135 (Kennett et al., 1995) phases in location
  Elevation and ellipticity corrections (Dziewonski and Gilbert, 1976; Kennett and Gudmundsson, 1996)
  Depth-phase bounce point corrections (Engdahl et al., 1998)
Accounts for correlated travel-time prediction errors
  Initial guess from Neighbourhood Algorithm search (Sambridge, 1999)
  Linearised inversion using a priori estimate of the full data covariance matrix (Bondár and McLaughlin, 2009)
Attempts for free-depth solution only if there is depth resolution
  Default depth is derived from historical seismicity
  Independent depth estimate from depth-phase stacking (Murphy and Barker, 2006)
Robust mb, MS magnitude estimates with uncertainties
  Gutenberg-Richter and Veith-Clawson depth-distance corrections for mb
Support for the ISC database schema
Support for IMS1.0 and ISF1.0 bulletin formats

## Slide 5: Initial Hypocentre
Reported hypocentres may exhibit a large scatter
Neighbourhood Algorithm (Sambridge and Kennett, 2001) to get an initial hypocentre
  Grid search around the median of reported hypocentre parameters
NA explores the search space and rapidly closes in on the global optimum
Once close to the global minimum, we switch to the linearised inversion algorithm to obtain the final solution and formal uncertainties

## Slide 6: Data Covariance Matrix
When correlated errors are present, the data covariance matrix is no longer diagonal
Off-diagonal elements account for correlated travel-time prediction errors due to similar ray paths
  Estimated by an isotropic stationary variogram (Bondár and McLaughlin, 2009) derived from GT residuals
The a priori picking error variances add to the diagonal
Generic variogram model

## Slide 7: Location Algorithm
A priori data covariance matrix describes both the picking errors and the correlated model error structure
We solve the equations in the eigensystem where the observations are independent (Bondár and McLaughlin, 2009; Bondár and Storchak, 2011)
Projection matrix
  Obtained from the inverse of the data covariance matrix
  Needs to be calculated only once
  Orthogonalises the data set and projects redundant observations to the null space
  Reduces the effective number of freedoms
Iterative linearised least squares using SVD
Accounting for correlated travel-time prediction errors
  Reduces location bias
  Provides reliable uncertainty estimates

## Slide 8: Depth Resolution
Attempt free-depth solution only if there is depth resolution
We have depth resolution if
  There is a local network
    one or more defining stations within 0.2°
  Or there are sufficient number of depth phases
    3 or more defining depth phases reported
  Or there are sufficient number of core reflections
    3 or more defining core reflections (PcP, ScP)
  Or there are sufficient number of local/near-regional S
    3 or more defining S and P pairs within 3°
Otherwise fix the depth to region-dependent default depth
Anthropogenic events are fixed to the surface
h=15 km
h=600 km

## Slide 9: Region-Dependent Default Depth
Defined on a 0.5x0.5 degree grid
Obtained from EHB and ISC (relocated with the new locator) free-depth solutions (~800K events)
Provides a reasonable default depth where there is seismicity

## Slide 10: ISC Locator Validation Tests
Relocation of the IASPEI Reference Event List
  ~7,200 GT0-5 events
  Typically very good azimuthal coverage
Relocation of the entire ISC bulletin (1960 – 2008)
  Good, bad and ugly network geometries
ISC bulletin
IASPEI Reference Event List

## Slide 11: GT Relocations
Minor improvements in location
Improvements in depth
Significant improvements in error ellipse coverage
Earthquakes (6,003)
Explosions (1,180)
New
Old

## Slide 12: Accounting for Correlated Errors
  With increasing number of stations:
  Area of error ellipse does not vanish
  Actual coverage is maintained
  Shape of error ellipse becomes more circular
  Location and depth bias is reduced for large number of stations
90% percentile
50% percentile
New
Old

## Slide 13: Fiji – Tonga - Kermadec
Reviewed ISC bulletin
Unreviewed locations with the new ISC locator

## Slide 14: Hindu Kush - Pamir
Reviewed ISC bulletin
Unreviewed locations with the new ISC locator

## Slide 15: Caucasus - Iran
Reviewed ISC bulletin
Unreviewed locations with the new ISC locator

## Slide 16: Tohoku, March – May, 2011

## Slide 17: iLoc features
Integrated RSTT travel-time predictions (Myers et al., 2010)
  RSTT predictions are used by default
  Pn/Sn and Pg/Lg travel time predictions can be turned on and off
Local velocity model
  Predictions for local phases are calculated up to a 3 degrees (default), beyond that iLoc switches to ak135/RSTT predictions
  Local phase TT predictions are calculated for Pg/Sg/Lg, Pb/Sb, Pn/Sn
Local ML and broadband mB magnitudes
  Murphy-Barker depth-distance corrections for mB
Support for the SeisComp3 database schema
  iLoc can read/write SeisComp3 MySQL database schema tables
Support for the new International Registry of Seismographic Stations conventions (FDSN standard A.D.S.L.)
  Agency.Deployment.Station.Location
Support for the new International Seismic Format (ISF2)
  Output file is always written as ISF2

## Slide 18: Regional Seismic Travel-Times (RSTT)
The RSTT rapid ray-tracing capabilities allow the use of realistic 3D models in routine operations
RSTT package (Myers et al., 2010)
  Developed by DoE labs LLNL, LANL and Sandia
  Global 3D upper mantle velocity model
  Crust: unified model in Eurasia and the Americas, Crust2.0 elsewhere
  Utilities for model tweaking
  Travel-time prediction utilities for regional (Pn/Sn) and first-arriving crustal (Pg/Lg) phases up to 15°
RSTT is fully integrated into iLoc
The virtual machine contains both iLoc and RSTT

## Slide 19: RSTT Relocation Tests
Relocated some 5,600 GT0-5 events in Eurasia
Most GT5 evens are very well recorded
  improvements are expected only in the tails
Clear improvements for GT0-2 explosions

## Slide 20: Improvements due to RSTT
More pronounced improvements with increasingly unbalanced networks
90% percentile
median

## Slide 21: NEIC PDE relocations with iLoc
The performance of iLoc was tested on the NEIC PDE bulletin from 2013-07-23 to 2014-05-21, altogether 10 months worth of data with more than 20 thousand events.
The PDE bulletin was relocated with ak135 travel-time predictions (NEIC also uses ak135) to compare the performance of iLoc and the NEIC locators, as well as with RSTT Pn/Sn predictions to see the improvements due to a 3D velocity model.

## Slide 22: Guatemala-Mexico border region
iLoc RSTT
PDE

## Slide 23: Guatemala-Mexico border region
iLoc RSTT
PDE
iLoc ak135
Better resolved subducting slab with RSTT predictions

## Slide 24: Chile-Peru-Bolivia border region
iLoc RSTT
PDE

## Slide 25: Chile-Peru-Bolivia border region
iLoc RSTT
PDE
iLoc ak135
Further improvements over ak135 due to RSTT predictions

## Slide 26: Chile-Argentina border region
iLoc RSTT
PDE

## Slide 27: Conclusions
The ISC locator
  Operational since January 2011 (events since January 2009)
  Provides honest ~85-90% actual coverage
  Reduces location bias due to correlated travel-time prediction errors
Better clustered event locations provide an improved view of the seismicity of the Earth
  Development continues as project iLoc
  iLoc uses RSTT predictions by default
  iLoc supports local velocity models
  iLoc is open source, available for download at ORFEUS
RSTT evaluation
  Pn/Sn predictions provide location improvements
  Mixing regional RSTT and teleseismic ak135 TT predictions does not introduce baseline differences